## Slide 1
ENGINEERING DESIGN INNOVATION
Base Subsystem — Drive & Layout
trolley footprint (above AMR)
4× mecanum wheels
FL
FR
RL
RR
arm extension rails (clamp subsystem)
36V 10Ah
● upward-facing VL53L0X time-of-flight distance sensor — one per corner
Why a mecanum base
Strafes sideways — lateral centring under the trolley is one direct move, no shuffling
Rotates in place — zero turning radius; directly answers the tow-tractor “needs turning space” gap from State of the Art
Same 4 wheels perform approach, orient and centre — no extra actuators
Sensing on the base
4× VL53L0X time-of-flight distance sensors face upward at the corners — front-left, front-right, rear-left, rear-right — connected through a TCA9548A I²C multiplexer. These alone drive the alignment sequence
Power chain
36V 10Ah battery feeds three buck converters in parallel — 24V, 12V and 5V rails, each tapped directly off the battery
Height budget: 190 mm measured vs ≤ 200 mm clearance — validated on physical chassis with metre rule

## Slide 2
ENGINEERING DESIGN INNOVATION
Control Architecture — Dual ESP32 over UART
BASE ESP32-S3 · coordinator
Docking state machine + safety monitor
Mecanum wheel mixing → 4× driving motors (BTS7960 drivers)
4× corner time-of-flight sensors via I²C multiplexer
AS5600 wheel encoders + BNO085 inertial measurement unit
ARM ESP32 · clamp subsystem
Arm extension belt motor + rails
Hook-flip servos
In-arm time-of-flight sensors (edge detection)
Limit switches (confirm travel only)
direct UART serial link
commands: extend · flip · release
acknowledge · limit status · faults
this serial link is the clamp-interface boundary in the firmware
FAILS SAFE: base ESP32 is the single clamp authority — no acknowledgement → no clamp motion · missed response → timeout → fault state (drive braked, clamp stopped)
Power distribution
36V 10Ah
battery
24V buck
12V buck
5V buck
36V bus
driving motors
(36V direct)
Driving motors and all three converter rails tap the 36V battery bus directly (parallel, not daisy-chained) — one converter failing cannot drag down another rail.

## Slide 3
ENGINEERING DESIGN INNOVATION
Alignment — Autonomous Centring Sequence
APPROACH
drive forward until a front-corner time-of-flight sensor sees the trolley's near edge
ORIENT
rotate toward the lagging corner until BOTH front corners see the board (yaw aligned, sensor-only)
CENTER_X
mark near edge, drive to far edge, return to the midpoint
CENTER_Y
strafe to find both side edges, drive to the midpoint
CONFIRM
all 4 corners in band, held for the full confirm period
CLAMP
handoff to arm ESP32 over the serial link — only if confirmed and no faults
any fault / per-phase timeout → FAULT: drive disabled + braked, clamp stopped · ABORT clears the latch → IDLE
How a corner “sees” the board Time-of-flight reading valid AND inside a height band, debounced over several samples — a single spike can't flip it. Solid trolley board → continuous, reliable returns.
Why centring is calibration-proof Both edges are measured by the same odometry integrator, and we drive to their midpoint — any calibration scale error cancels out.
SAFETY INTERLOCK — the clamp physically cannot engage unless:
alignment CONFIRMED (sustained) && no motor / overcurrent fault. Limit switches confirm clamp travel only — they never authorise clamping.

## Slide 4
ENGINEERING DESIGN INNOVATION
Base Subsystem — Test Plan & Validation
Base test | Requirement | Protocol | Pass criteria | Status
Height clearance | ≤ 200 mm | Side-profile measurement with metre rule + photo evidence | 190 mm → 10 mm margin | Measured — confirm photo
Worst-case caster misalignment | Moves for all 4 caster orientations | Manually misalign all 4 trolley casters, command straight drive | Moves off cleanly, no wheel slip (model: 3.0× traction margin) | Planned
Loaded movement | ≥ 100 kg payload | Timed 10 m drive, 100 kg deadweight, Fablab floor | Completes run without stall or slip | Planned
Speed under load | ≥ 0.3 m/s (target 0.5–0.7) | Distance-over-time across 5 m, fully loaded | v ≥ 0.5 m/s (model: 4.4× torque margin) | Planned
Alignment repeatability | Centred before clamp | 10 docking runs from randomised offset + rotation starts | CONFIRM state reached every run; centring offset within tolerance — report mean ± standard deviation | NEW — add
Serial link fail-safe | No unsafe clamp action | Disconnect the serial wires between the two ESP32s mid-docking | Zero clamp motion; fault state within timeout; drive braked | NEW — add
Fault injection | Safe stop from any state | Trigger a motor / overcurrent fault during drive and during clamp handoff | Drive braked + clamp stopped; restart only after explicit ABORT clear | NEW — add
Mirror the clamp-force experiment format: at least 5 trials per test, report mean ± standard deviation and pass rate — the same statistical rigour reviewers saw on the clamping slide.